		Human	Rat/Mouse
fenestration / radius / size 12{ { {r rSub { size 8{ ital "fen"} } rSup { size 8{ ital "old"} } } over {r rSub { size 8{ ital "fen"} } rSup { size 8{ ital "young"} } } } } {} / porosity / size 12{ { {f rSub { size 8{ ital "fen"} } rSup { size 8{ ital "old"} } } over {f rSub { size 8{ ital "fen"} } rSup { size 8{ ital "young"} } } } } {} / frequency / size 12{ { {N rSub { size 8{ ital "fen"} } rSup { size 8{ ital "old"} } } over {N rSub { size 8{ ital "fen"} } rSup { size 8{ ital "young"} } } } } {}	1.0 / old (60 years)/young (20 years) / 0.25 / old (60 years)/young (20 years) / 0.25 / old (60 years)/young (20 years) / (calculated from changes in r and f)	diameter / 58±1nm (young, baboon), 70±2nm (old, baboon), old/young 1.21 / porosity / determined by scanning electron microscopy / 4.2±0.5% (young, baboon), 2.4±0.4% (old, baboon), old/young 0.61 / frequency / determined by transmission electron microscopy / 7.7±0.7 [1/µm] (young, human), 1.5±0.4 [1/µm] (old, human), old/young 0.19 / 9.4±0.9 [1/µm] (young, baboon), 5.5±0.7 [1/µm] (old, baboon), old/young 0.58	diameter / 73±1nm (young, rat), 60±1nm (old,rat), old/young 0.82 / 74±4nm (young, mouse), 58±12nm (old,mouse), old/young 0.78 / porosity / determined by scanning electron microscopy / 4.1±2.3% (young, rat), 2.5±1.2% (old, rat), old/young 0.61 / 4.1±2.2% (young, mouse), 2.2±3.5% (old mouse), old/young 0.54 / frequency / determined by transmission electron microscopy / 2.7±1.1 [1/µm] (young, rat), 0.9±0.8 [1/µm] (old, rat), old/young 0.33
endothelial thickness / size 12{ { {y rSub { size 8{ ital "end"} } rSup { size 8{ ital "old"} } } over {y rSub { size 8{ ital "end"} } rSup { size 8{ ital "young"} } } } } {}	1.75 / old (60 years)/young (20 years)	Determined by transmission electron microscopy / 165±17nm (human, young), 289±9nm (human, old), old/young 1.75 / 130±8nm (baboon, young), 186±9nm (baboon, old) , old/young 1.43	Determined by transmission electron microscopy / 230±50nm (rat, young), 320±80nm (rat, old) , old/young 1.39 / 154±4nm (mouse, young), 245±8nm (mouse, old), old/young 1.59